## Slide 1: Composites
Dr. Ranjit Kumar
Department of Chemical Engineering
Email: ranjit.kumar@snu.edu.in

## Slide 2: Composites
Combine materials with the objective of getting a more desirable combination of properties
  Ex: get flexibility & weight of a polymer plus the strength of a ceramic
Principle of combined action
  Mixture gives “averaged” properties
Notes:   Don’t always get what you want
    Ex: combine ferret (pet) + mink (fur)
      Desire a mink with good disposition but got a nasty ferret

## Slide 3: Matrix and Dispersed Phase
Schematic representations of the various geometrical and spatial characteristics of particles of the dispersed phase that may influence the properties of composites: (a) concentration, (b) size, (c) shape, (d) distribution, and (e) orientation.

## Slide 4: Terminology/Classification
• Composites:
-- Multiphase material w/significant
proportions of each phase.
• Dispersed phase:
-- Purpose: enhance matrix properties.
-- Classification: Particle, fiber, structural
• Matrix:
-- The continuous phase
-- Purpose is to:
- transfer stress to other phases
- protect phases from environment
-- Classification: MMC, CMC, PMC
metal
ceramic
polymer
woven
fibers
cross
section
view
0.5
mm
0.5
mm

## Slide 5: Composite

## Slide 6: Composite Survey: Particle
• Examples:
- Spheroidite
steel
matrix:
ferrite (a)
(ductile)
particles:
cementite
(
Fe
3
C
)
(brittle)
60 mm
- WC/Co
cemented
carbide
matrix:
cobalt
(ductile)
particles:
WC
(brittle,
hard)
V
m
:
10-15 vol%!
600 mm
- Automobile
tires
matrix:
rubber
(compliant)
particles:
C
(stiffer)
0.75 mm
Particle-reinforced
Fiber-reinforced
Structural

## Slide 7: Composite Survey: Fiber
Fiber Materials
  Whiskers - Thin single crystals - large length to diameter ratio
    graphite, SiN, SiC
    high crystal perfection – extremely strong, strongest known
    very expensive
Particle-reinforced
Fiber-reinforced
Structural
  Fibers
    polycrystalline or amorphous
    generally polymers or ceramics
    Ex: Al2O3 , Aramid, E-glass, Boron, UHMWPE
  Wires
    Metal – steel, Mo, W

## Slide 8: Composite Survey: Structural
• Stacked and bonded fiber-reinforced sheets
-- stacking sequence: e.g., 0º/90º
-- benefit: balanced, in-plane stiffness
Particle-reinforced
Fiber-reinforced
Structural
• Sandwich panels
-- low density, honeycomb core
-- benefit: small weight, large bending stiffness
honeycomb
adhesive layer
face sheet